## Slide 1: Computer Networks
Zhiqing Huang
School of Software Engineering
Beijing University of Technology

## Slide 2: Chapter 4 Medium Access Control Sublayer

## Slide 3: Medium Access Control Sublayer
Channel allocation problem
Multiple access protocols
Wireless LAN protocols
Ethernet
Wireless LANs
Broadband wireless
Bluetooth
RFID
Data link layer switching

## Slide 4: The MAC Sublayer
Responsible for deciding who sends next on a multi-access link
  An important part of the link layer, especially for LANs
Physical
Link
Network
Transport
Application
MAC is in here!

## Slide 5: Channel Allocation Problem
Fixed channel, traffic from multiple users
  Divide up bandwidth using FTM, TDM, CDMA, etc.
  A static allocation, e.g., FM radio
Static allocation performs poorly for bursty traffic
  Allocation to a user sometimes goes unused

## Slide 6: Channel Allocation Problem (2)
Dynamic allocation assigns the channel to a user when the user needs it
  Potentially N times as efficient for N users
Schemes vary with assumptions
Assumption | Implication
Independent traffic | Often not a good model, but permits analysis
Single channel | No external way to coordinate senders
Observable collisions | Needed for reliability; mechanisms vary
Continuous or slotted time | Slotting may improve performance
Carrier sense | Can improve performance if available

## Slide 7: Dynamic Channel Allocation in LANs and MANs
Assumptions
  Station model assumption
    Stations are responsible for data transmission
  Single channel assumption
    All stations use a single channel for both sending and receiving
  Collision assumption
    Simultaneous transmissions cause collision which can be detected
    Affected frames must be retransmitted
  Continuous or slotted time
    Frames can be transmitted continuously or at slotted times
  With or without carrier sense
    Stations can or cannot detect whether the transmission channel is currently being used

## Slide 8: Multiple Access Protocols
ALOHA
CSMA (Carrier Sense Multiple Access)
Collision-free protocols
Limited-contention protocols
Wireless LAN protocols

## Slide 9: ALOHA
In pure ALOHA, users transmit frames whenever they have data
  Users retry after a random amount of time for collisions
Efficient and low delay in low load environment
Collision
Collision
Time
User
A
B
C
D
E

## Slide 10: ALOHA (2)
Collisions happen when other users transmit during a vulnerable period that is twice the frame time
  Synchronizing senders to slots can reduce collisions

## Slide 11: ALOHA (3)
Slotted ALOHA is twice as efficient as pure ALOHA
  Low load wastes slots, high loads causes collisions
  Efficiency up to 1/e (37%) for random traffic models

## Slide 12: CSMA (Carrier Sense Multiple Access)
CSMA improves on ALOHA by sensing the channel
  User doesn’t send if it senses someone else is sending
Variations on what to do if the channel is busy
  1-persistent (greedy) sends as soon as the channel becomes idle
  Non-persistent waits for a random amount of time before trying again
  p-persistent sends with probability p when idle

## Slide 13: CSMA (2)
1-persistent CSMA
  If idle, transmit
  If not idle, continuously sense until the channel becomes idle
Non-persistent CSMA
  If idle, transmit
  If not idle, wait for a random amount of time, then repeat the whole process

## Slide 14: CSMA (3)
p-persistent CSMA
  Applicable to slotted channels
  If idle, transmit with probability p (and defer the transmission until the next slot with probability 1-p)
  If not idle, wait for the next slot
  If collision occurs, wait for a random amount of time

## Slide 15: CSMA (4)
CSMA outperforms ALOHA
Being less persistent is better under high load

## Slide 16: CSMA with Collision Detection
CSMA/CD improvement is due to aborting transmission upon detecting collision
  Reduce contention time to improve performance
Collision time is much shorter than frame time

## Slide 17: Collision-Free Protocols - Bitmap
Collision-free protocols avoid collisions completely
  Sender must know when is its turn to send
The basic bit-map protocol
  Sender sets a bit in contention slot if it has data
  Senders send in turn
  Everyone knows who has data to send

## Slide 18: Collision-Free Protocols – Token Ring
Token sent round a ring determines the sending order
  Station with token may send a frame before passing it
  Idea can be used without ring too, e.g., token bus
Station
Direction of
transmission
Token

## Slide 19: Limited-Contention Protocols
Divide stations into groups within which only a very small number are likely to send
Already too many contenders for a good chance of one winner

## Slide 20: Wireless LAN Protocols
Wireless is more complicated compared to wired
Nodes may have different coverage regions
  Lead to hidden and exposed nodes
Nodes cannot detect collisions, i.e., sense while sending
  Makes collisions expensive and better to be avoided

## Slide 21: Wireless LAN Protocols (2)
A wireless LAN
  (a) A is transmitting
  (b) B is transmitting

## Slide 22: Wireless LAN Protocols – Hidden Nodes
Hidden nodes are senders that cannot sense each other but nonetheless collide at intended receiver
  A and C are hidden nodes when sending to B
  Consequence: loss of efficiency

## Slide 23: Wireless LAN Protocols – Exposed Nodes
Exposed nodes are senders who can sense each other but can still transmit safely (to different receivers)
  B  A and C  D are exposed nodes
  Desirable concurrency: improve performance

## Slide 24: Wireless LAN Protocols - MACA
Multiple Access with Collision Avoidance protocol
  A sends RTS to B [left]; B replies with CTS [right]
  A sends RTS to B; C and E hear and defer for CTS
  B replies with CTS; D and E hear and defer for data

## Slide 25: Ethernet
Classic Ethernet
Switched/Fast Ethernet
Gigabit/10 Gigabit Ethernet

## Slide 26: Ethernet Cabling
The most common kinds of Ethernet cabling

## Slide 27: Classic Ethernet – Physical Layer
One shared coaxial cable to which all hosts attached
  Up to 10 Mbps, with Manchester encoding
  Hosts ran the classic Ethernet protocol for access

## Slide 28: Classic Ethernet – MAC
MAC protocol is 1-persistent CSMA/CD (earlier)
  Random delay (backoff) is computed with BEB (Binary Exponential Backoff) after collision
  Frame format is still used in modern Ethernet
Ethernet
(DIX)
IEEE 802.3

## Slide 29: Classic Ethernet - MAC (2)
CSMA/CD
Collisions can occur and take as long as 2 to detect
   is the time it takes to propagate over the Ethernet
  Leads to minimum packet size for reliable detection

## Slide 30: Classic Ethernet - Performance
Efficient for large frames, even with many senders
  Degrades for small frames (and long LANs)

## Slide 31: Switched/Fast Ethernet
Copyright @ Jingsha He 2004-2015
31
Hubs join all lines to form a single CSMA/CD domain
Switches isolate ports to form separate domains
  Much greater throughput for multiple ports
  No need for CSMA/CD with full-duplex lines
November 4, 2017

## Slide 32: Switched/Fast Ethernet (2)
Switches be wired to computers, hubs and switches
  Hubs concentrate traffic from computers
Switch
Twisted pair
Switch ports
Hub

## Slide 33: Switched/Fast Ethernet (3)
Fast Ethernet extends Ethernet from 10Mbps to 100 Mbps
  Twisted pair (with Cat 5) has dominated the market

## Slide 34: Gigabit / 10 Gigabit Ethernet
Switched Gigabit Ethernet has become the mainstream
  With full-duplex lines between computers/switches

## Slide 35: Gigabit / 10 Gigabit Ethernet (2)
  Gigabit Ethernet is commonly run over twisted pair
  10 Gigabit Ethernet is being deployed where needed
40/100 Gigabit Ethernet is under development

## Slide 36: Wireless LANs
802.11 architecture/protocol stack
802.11 physical layer
802.11 MAC
802.11 frames
November 4, 2017
Copyright @ Jingsha He 2004-2015
36

## Slide 37: 802.11 Architecture/Protocol Stack
Copyright @ Jingsha He 2004-2015
37
Wireless clients associate to a wired access point (AP)
  Called infrastructure mode
  Without an AP: called ad-hoc mode, but that is the future
November 4, 2017
Access Point
Client
To Network

## Slide 38: 802.11 Architecture/Protocol Stack (2)
Copyright @ Jingsha He 2004-2015
38
MAC is used across different physical layers
November 4, 2017

## Slide 39: 802.11 Physical Layer
Copyright @ Jingsha He 2004-2015
39
NICs are compatible with multiple physical layers, e.g., 802.11 a/b/g
November 4, 2017
Name | Technique | Max. Bit Rate
802.11b | Spread spectrum, 2.4 GHz | 11 Mbps
802.11g | OFDM, 2.4 GHz | 54 Mbps
802.11a | OFDM, 5 GHz | 54 Mbps
802.11n | OFDM with MIMO, 2.4/5 GHz | 600 Mbps

## Slide 40: 802.11 MAC
Copyright @ Jingsha He 2004-2015
40
CSMA/CA inserts backoff slots to avoid collisions
MAC uses ACKs/retransmissions for wireless errors
November 4, 2017

## Slide 41: 802.11 MAC (2)
Copyright @ Jingsha He 2004-2015
41
Virtual channel sensing with the NAV (network allocation vector) and optional RTS/CTS (often not used) avoids hidden terminals
November 4, 2017

## Slide 42: 802.11 MAC (3)
Copyright @ Jingsha He 2004-2015
42
Different backoff slot times support quality of service
  Short intervals are given to preferred access, e.g., control, VoIP
MAC also has other mechanisms, e.g., power save
November 4, 2017

## Slide 43: 802.11 Frames
Copyright @ Jingsha He 2004-2015
43
Frames have different types specified by “Frame control”
Data frames have 3 addresses to pass via APs
November 4, 2017

## Slide 44: Broadband Wireless
802.16 architecture/protocol stack
802.16 physical layer
802.16 MAC
802.16 frames

## Slide 45: 802.16 Architecture/Protocol Stack
Wireless clients connect to a wired base station (like 3G)

## Slide 46: 802.16 Architecture/Protocol Stack (2)
MAC is connection-oriented
IP is connectionless
Convergence sublayer maps between the two

## Slide 47: 802.16 Physical Layer
Based on OFDM (Orthogonal Frequency Division Multiplexing)
  Base station gives mobile terminals bursts (subcarrier/time frame slots) for uplink and downlink

## Slide 48: 802.16 MAC
Copyright @ Jingsha He 2004-2015
48
Connection-oriented with base station in control
  Clients request the bandwidth in need
Different kinds of service can be requested
  Constant bit rate, e.g., uncompressed voice
  Real-time variable bit rate, e.g., video, Web
  Non-real-time variable bit rate, e.g., file download
  Best-effort for everything else
November 4, 2017

## Slide 49: 802.16 Frames
Copyright @ Jingsha He 2004-2015
49
Frames vary depending on their type
Connection ID instead of source/destination addresses
November 4, 2017
(a) A generic frame. (b) A bandwidth request frame
(b)
(a)

## Slide 50: Bluetooth
Bluetooth architecture
Bluetooth applications/protocol
Bluetooth radio/link layers
Bluetooth frames

## Slide 51: Bluetooth Architecture
Piconet master is connected to slave wireless devices
  Slaves may go into sleep (parked) to save power
  Two piconets can be bridged into a scatternet

## Slide 52: Bluetooth Applications/Protocol Stack
Profiles give the set of protocols for a given application
  25 profiles in total: headset, intercom, streaming audio, remote control, personal area network, etc.

## Slide 53: Bluetooth Radio/Link Layers
Radio layer
  Uses adaptive frequency hopping in 2.4 GHz band
Link layer
  TDM with timeslots for master and slaves
  SCO (synchronous connection oriented) for periodic slots in each direction
  ACL (asynchronous connectionless) for packet-switched data
  Links undergo pairing (user confirms passkey/PIN) to authorize the user before use

## Slide 54: Bluetooth Frames
Time is slotted
Enhanced data rates send faster but for the same time
Addresses are only 3 bits (for 8 devices)
(b)
(a)
(a)
(b)

## Slide 55: RFID *
EPC Gen 2 architecture
EPC Gen 2 physical layer
EPC Gen 2 Tag Identification layer
EPC Gen 2 frames

## Slide 56: EPC Gen 2 Architecture
Reader signal powers tags
Tags reply with backscatter

## Slide 57: EPC Gen 2 Physical Layer
Reader uses duration of on period to send 0/1
Tag backscatters reader signal in pulses to send 0/1

## Slide 58: EPC Gen 2 Tag Identification Layer
Reader sends query and sets slot structure
Tags reply (RN16) in a random slot (may collide)
Reader asks one tag for its identifier (Ack)
Process continues until no tags are left

## Slide 59: EPC Gen 2 Frames
Reader frames vary based on type (Command)
  Query shown below with parameters and error detection
Tag responses are simply data
  Reader sets timing and knows the expected format

## Slide 60: Data Link Layer Switching
Uses of bridges
Learning bridges
Spanning tree
Repeaters, hubs, bridges, routers and gateways
Virtual LANs

## Slide 61: Uses of Bridges
Common setup is a building with centralized wiring
  Bridges (switches) are placed in or near wiring closets

## Slide 62: Uses of Bridges (2)
Multiple LANs can be connected by bridges to handle load that is higher than the capacity of a single LAN

## Slide 63: Uses of Bridges (3)
A configuration with four LANs and two bridges

## Slide 64: Learning Bridges
A bridge can be operated as a switched LAN (not a hub)
  Computers, bridges and hubs connect to its ports

## Slide 65: Learning Bridges (2)
Backward learning algorithm picks the output port
  Source address in a frame is associated with the input port
  Frame with destination address is sent to the learned port
  Frame with an unlearned destination is sent to all ports except the input port
  Frame is discarded if destination port is the same as the source port
No need for configuration
  Forget unused addresses to allow changes
  Bandwidth efficient for two-way traffic

## Slide 66: Learning Bridges (3)
Bridges extend the data link layer
  Use but don’t remove Ethernet header/addresses
  Don’t inspect the network header

## Slide 67: Spanning Tree
Problem
  Bridge topologies may contain loops
  Backward learning may cause frames to circulate for ever
  Spanning tree support is needed to solve the problem

## Slide 68: Spanning Tree (2)
Only a subset of the forwarding ports is used for data to avoid loops
The subset can be selected using a spanning tree distributed algorithm

## Slide 69: Repeaters, Hubs, Bridges, Switches, Routers and Gateways
Devices are named according to the layer they work
  Bridge and switch operate in the data link layer
(a) Which device is in which layer
(b) Frames, packets and headers

## Slide 70: Repeaters, Hubs, Bridges, Switches, Routers and Gateways (2)
(a) Hub
(b) Bridge
(c) Switch

## Slide 71: Virtual LANs
A building with centralized wiring using hubs and a switch

## Slide 72: Virtual LANs (2)
VLANs (Virtual LANs) split one physical LAN into multiple logical LANs to ease management tasks
  Ports are assigned to the VLAN that they belong

## Slide 73: Virtual LANs (3)
Four physical LANs can be organized into two VLANs (gray and white) by two bridges, as in (a)
The same 15 machines can also be organized into two VLANs by switches, as in (b)

## Slide 74: Virtual LANs - IEEE 802.1Q
Bridges need to be aware of VLANs to support them
  In 802.1Q, frames contain a VLAN tag
  Legacy switches with no tags are also supported

## Slide 75: Virtual LANs - IEEE 802.1Q (2)
802.1Q frames carry a tag (VLAN identifier)
  Length/Type value is 0x8100 for VLAN protocol

## Slide 76: Q & A